## Slide 1
HACKERING 2.0 | REAL-TIME VOICE AI TRACK
NeuroVocal AI
An Emergency Triage Voice System That Listens to the Physics of Your Vocal Cords
Most voice bots only listen to the words callers say. NeuroVocal AI runs two processes at once:
1. An empathetic emergency operator that talks with the patient and coordinates location. 2. A real-time digital signal processing (DSP) engine that scans raw microphone audio for vocal fold tremors, hypoxia, and acute stroke symptoms at 25 Hz.
Built by Harish & Team | RV College of Engineering | Round 1 Project Pitch

## Slide 2
The Problem in Real Emergency Calls: When Words Lie
Why standard AI voice assistants fail when human callers are having an acute medical crisis.
WHAT STANDARD VOICE BOTS DO
• Listens only to transcribed words (Speech-to-Text). • When a patient says: 'I just feel a bit tired and lightheaded today', the bot assumes mild exhaustion. • Recommends resting, drinking water, or booking a routine clinic visit. • By the time an ambulance is called, the 4.5-hour stroke treatment window has closed.
WHAT NEUROVOCAL AI HEARS
• Inspects the raw audio physics behind their voice. • The caller may sound calm, but facial paralysis causes unilateral vocal tract asymmetry. • Formants F1 and F2 collapse into 1500 Hz (dysarthric vowel slur). • Jitter spikes above 2.5% due to vocal fold tremors. • Instantly alerts the dispatcher: 'CODE RED: SUSPECTED STROKE'.

## Slide 3
The Solution: Dual-Stream Real-Time Architecture
Two dedicated tasks running in parallel over the exact same microphone audio stream.
STREAM 1: The Conversational Operator
• Deepgram Nova-2: Real-time speech transcription (< 250ms). • Groq Llama 3.3 70B: Fast clinical triage logic. Keeps answers under 25 words to avoid panicking the caller. • Cartesia Sonic: Empathetic, human-like voice synthesis (< 150ms). • Goal: Asks for location, confirms patient posture, keeps them calm.
STREAM 2: The Acoustic Health Scanner
• 16 kHz Circular Ring Buffer: Captures audio frames in memory. • 25 Hz DSP Engine: Slides a 64 ms analysis window every 40 ms. • Mathematical Extraction: Calculates F0 pitch, jitter, HNR, and LPC formants without LLM overhead. • WebSocket Broadcast: Sends live JSON telemetry to dispatcher HUD.
Key Engineering Principle: The DSP scanner runs asynchronously. The conversational bot never stutters, and the medical telemetry never lags.

## Slide 4
The Audio Physics: What We Listen For
Four clinical biomarkers extracted in real time from live speech signals.
1. Fundamental Pitch (F0)
Tracks vocal cord frequency Normal: 85 - 255 Hz Clinical insight: Rapid tremor indicates acute shock or autonomic panic.
2. Jitter (Perturbation)
Cycle-to-cycle frequency variation Normal: < 1.04% | Alert: > 2.50% Clinical insight: Vocal fold weakness from unilateral facial stroke causes jitter to spike.
3. Harmonics-to-Noise (HNR)
Voice purity vs. turbulent air Normal: > 18 dB | Critical: < 12 dB Clinical insight: When lungs lack oxygen (hypoxia), turbulent breath noise takes over.
4. Formants (F1, F2)
Vocal tract resonant shapes Healthy vowels disperse widely Clinical insight: Dysarthria (slurring) collapses tongue movement: F2 centralizes to 1500 Hz.

## Slide 5
Real Scenario: Catching an Acute Stroke Live
How NeuroVocal AI turns a misclassified routine call into a life-saving dispatch.
Step 1: The Caller
An elderly caller rings helpline 112: 'Hello... I feel a bit lightheaded, and my right hand feels heavy.'
Step 2: Stream 1 Keeps Them Calm
The conversational bot replies gently: 'I hear you. Please stay seated right where you are. What is your address?'
Step 3: Stream 2 Detects Vocal Collapse
The DSP scanner notes the caller's vowel space symmetry dropped 35% and F2 collapsed to 1490 Hz with 15% jitter.
Step 4: Dispatcher Emergency Alert
The hospital dashboard flashes: 'CODE RED: ACUTE STROKE BIOMARKER DETECTED' with immediate GPS coordinates.

## Slide 6
Engineering Deep-Dive: 25 Hz Real-Time Telemetry
Actual benchmark numbers tested on our laptop hardware with test_client.py.
25.17 Hz
Measured Delivery Rate
Target: 25.0 Hz (every 40 ms)
40.00 ms
Average Packet Interval
Standard deviation: 0.54 ms
0.62 ms
Total Clock Drift
Zero latency accumulation over 4.0s
HOW WE PREVENTED AUDIO LATENCY PILEUP
1. Circular Ring Buffer: A 16 kHz fixed audio buffer holds the most recent 0.5 seconds of audio. New microphone samples overwrite the oldest samples in O(1) time. 2. Non-blocking WebSocket Dispatch: In server.py, we broadcast to clients with a 35ms timeout. If a client device temporarily slows down, stale packets are dropped rather than buffered. 3. Hardware-Independent: Works with built-in laptop microphones, smartphone mics, or standard phone lines without needing medical sensors.

## Slide 7
How to Test Our Project Live
Everything is ready to run locally right now.
RUNNING THE SYSTEM (3 SIMPLE STEPS)
1. Launch the Backend Server: > python server.py Starts the FastAPI WebSocket server on http://localhost:8000 and taps the laptop microphone. 2. Open the Dispatcher HUD in Browser: > Visit http://localhost:8000/client Watch live F0, Jitter, HNR, and Formants stream at 25 Hz. Click 'Stroke / Dysarthria' to watch the CSI score jump to 0.80 and trigger the CODE RED emergency alert. 3. Run the Automated Latency Benchmark: > python test_client.py Measures 100 consecutive frames to verify 25 Hz streaming and 0 ms latency drift.